# IPv4 Datagram Fragmentation and Delays
Why IPv4 Datagram Fragmentation required?	Different Networks may have different maximum transmission unit (MTU)
How is Fragmentation done?	When a packet is received at the router, destination address is examined and MTU is determined. / If size of the packet is bigger than the MTU, and the ‘Do not Fragment (DF)’ bit is set to 0 in header, then the packet is fragmented into parts and sent one by one. / The maximum size of each fragment is the MTU minus the IP header size / ip header size is from 20 to 60 Bytes / Each fragment is converted to a packet / the following changes happen in the datagram header: / The total length field is changed to the size of the fragment. / The More Fragment bit (MF bit) is set for all the fragment packets except the last one. / The fragment offset field is set, based on the number of fragment that is being set and the MTU. / Header Checksum is re-calculated. / all fragments would be having same identification number
Delays	Processing delay: Time taken by the routers to process the data packet header.
	Queuing delay: Time taken by the data packet in routing queues.
	Transmission delay: Time taken to load a data packet onto the transmission channel / Dt = N/R / N: Number of bits to be transmitted / R: Rate or transmission speed of the channel
	Propagation delay – Time taken by the data packet to reach from source to destination / Dp = D/S, / D: Distance between the source and the destination / S: is the speed of propagation