# IPv4 Datagram Header
Responsibilities of Network Layer:	Packet forwarding/Routing of packets:
	Connectionless communication(IP)
	Fragmentation of data packets: Splitting of data packets that are too large to be transmitted on the network
two types of network transmission techniques	circuit switched / Circuit switched network, a single path is designated for transmission of all the data packets. / received in order / Packet switched / each packet may be sent through a different path to reach the destination. / may be received out of order
IPv4:	connectionless protocol used for packet-switched networks. / best effort delivery mode / It provides a logical connection between network devices by providing identification for each device. / manual and automatic configurations / IPv4 is defined and specified in IETF publication RFC 791.
best effort delivery mode	neither delivery is guaranteed / nor proper sequencing or avoidance of duplicate delivery is assured.
IPv4 Datagram Header	Size of the header is 20 to 60 bytes.
Data is from 20 bytes to 65536 Bytes
VERSION	Version of the IP protocol (4 bits)
HLEN	IP header length (4 bits) / The minimum value for this field is 5 and the maximum is 15.
Type of service:	Low Delay, High Throughput, Reliability (8 bits)
Total Length:	Length of header + Data
Identification	Unique Packet Id for identifying the group of fragments of a single IP datagram (16 bits)
Flags	3 flags of 1 bit each / reserved bit (must be zero) / do not fragment flag / more fragments flag (same order)
Fragment Offset:
Time to live:	Datagram’s lifetime (8 bits), It prevents the datagram to loop through the network by restricting the number of Hops
Protocol	Name of the protocol t 8 Bits
Header Checksum:	16 bits header checksum for checking errors in the datagram header
Source IP address:	32 bits IP address of the sender
Destination IP address:	32 bits IP address of the reciver
Option	Optional information such as source route, record route. / Used by the Network administrator to check whether a path is working or not. / From 0 to 40 Bytes