# Collision Domain and Broadcast Domain in Computer Network
hub is a multiple-port repeater	switch is a multiple-port bridge
Collision Domain	Broadcast Domain
in a situation where two devices send out their messages simultaneously, a collision will occur leading them to wait and re-transmit their messages / it happens only in the case of a half-duplex mode.	A Broadcast Domain is a scenario in which when a device sends out a broadcast message, all the devices present in its broadcast domain have to pay attention to it. / This creates a lot of congestion in the network / affects the bandwidth
which of our network devices break collision domains, and which of them break broadcast domains?
HUB	Hubs do not segment a network / hub is neither a collision domain separator nor a broadcast domain separator / All the devices connected to a hub are in a single collision and single broadcast domain.
SWITCH	Every port on a switch is in a different collision domain / a switch is a collision domain separator / All the ports on the switch are still in a single broadcast domain. If a device sends a broadcast message, it will still cause congestion.
ROUTER	A router not only breaks collision domains but also breaks broadcast domains / A router creates a connection between two networks. / A broadcast message from one network will never reach the other one as the router will never let it pass.